## Slide 1
Autonomous Plastic
Waste Collector Robot
EEE400B Project Presentation
Team Members
MD. Nahid Hassan (2022-1-80-037)
MD. Mainuddin Rahman Eshan (2022-2-80-022)
Faisal Hasan (2022-2-80-007)
Niaz Morshed Razon (2022-2-80-008)
Supervisor: Dr. Ratil Hasnat
Associate Professor Department of EEE
East West University
1

## Slide 2
Stakeholders Reviews
Individuals from different sectors were consulted to gather feedback for the project design
🏭 Recycling & Plastic Processing Industry
Clean recyclable plastic specifically PET bottles, proper collection.
🌍 Environmental / NGO
Waste reduction, environmental compliance, sustainability
♻️ Local Scrap Business Owners
Low-cost operation, easy maintenance, recyclable plastic focus
👥 General Public / Park Users
Safety, low noise, non-intrusive operation, visible warning indicators
2

## Slide 3
Functional Requirements
Core system capabilities required for operation
1
Autonomous Navigation
No human control required — fully self-guided movement
2
Plastic Detection
Camera + AI-based identification of plastic waste
3
Waste Pickup Mechanism
Automated physical collection of detected waste
4
Onboard Storage & Auto Return
Stores collected waste; returns autonomously when full
3

## Slide 4
Overall System Architecture
To ensure proper functionality the whole system is divided into multiple subsystem
Subsystem | Function
Power Management Unit | Supplies regulated voltage to controllers, sensors, motors, and actuators
Plastic Detection Unit | Uses camera-based vision to detect plastic waste and generate object position data
Control & Processing Unit | Processes detection and sensor data, then makes navigation and pickup decisions
Navigation & Mobility Unit | Moves the robot, avoids obstacles, and positions the robot near the detected waste
Waste Collection Mechanism | Picks up the detected plastic object and transfers it to storage
Storage Unit | Stores collected plastic waste and supports unloading into a disposal point
Safety & Monitoring Unit | Monitors obstacles, battery condition, and emergency situations
4

## Slide 5
Solutions for Plastic Detection
Traditional Vision
HSV + Edge Detection + Texture
Use threshold values of color and shape
Use RGB color spectrum
Deep Learning
YOLOv8n Model
Use Image dataset
Trained to detect plastic bottles
Hybrid Detection
Tiny YOLO + Image Filtering
Medium complexity
Cost-effective
5
D = Distance from camera to object (in cm)
f = Focal length of the camera (in pixels)
H = Real-world height/width of the object
h = Height of the bounding box of the detected object in the image (in pixels)
Distance Measurement : (Monocular Vision Ranging)

## Slide 6
Plastic Detection
1. Traditional Vison: HSV color segmentation + edge + shape analysis
Traditional vision uses HSV color segmentation, edge detection, and shape analysis to identify plastic-like regions from camera input.
6

## Slide 7
Plastic Detection
2. YOLOV8n Deep-learning object detection model
YOLOv8n, trained on a plastic waste dataset, detects plastic objects from camera input and provides bounding box coordinates with confidence scores for precise pickup.
7

## Slide 8
Plastic Detection
3: Hybrid Detection
+
YOLO Detection
HSV Filtering
Refined Detection
=
YOLO detects candidate objects, and HSV filtering validates them to remove false positives and improve precision.
8

## Slide 9
Comparison & Final Selection — Detection
Parameter | Traditional HSV | YOLOv8n | Hybrid
Accuracy | 66% | 82% | 85%
Precision | 67.8% | 86.67% | 89.8%
Recall | 61% | 84.78% | 79%
False Positive Rate | 29% | 12% | 9%
Computational cost | Low | High | High
Reliability | Low (lighting sensitive) | High (robust) | Medium
✅ Selected Solution: YOLOv8n Deep Learning-Based Detection
9
Notes: Computational cost

## Slide 10
Sub-system solutions — Navigation
LiDAR-Based Navigation
Sensor: LIDAR
Uses high-resolution
360° scanning to create
Sharp grid maps for
accurate navigation
and path planning.
Ultrasonic-Based Navigation
Sensor: Ultrasonic Sensors
Uses multi-sensor
distance measurement
to detect obstacles,
but provides coarse
and noisy environment mapping.
Feature
Sensor-based mapping for dynamic environment adaptation.
Capabilities
Safe motion via real-time static & dynamic obstacle avoidance
Goal
Navigate autonomously without human control.
10

## Slide 11
LiDAR-Based Navigation
Ultrasonic-Based Navigation
Comparison of Sensor-based Grid mapping
11

## Slide 12
Overall Comparison & Final Selection — Navigation
Criteria | LiDAR System | Ultrasonic System
Accuracy | ~90% (High) | ~75–80% (Medium)
Cost | High | Low
Computational Load | High | Low
Response Time | ~0.1s | ~0.1–0.3s
Motion Smoothness | ~95% | ~87%
Tracking Error | Very Low (~cm) | Low (~few cm)
Selected Solution: LiDAR-Based Navigation
Justify: LiDAR for its high-accuracy mapping, sharp grid-based environment analysis, and reliable navigation in dynamic conditions.
12

## Slide 13
Waste Collection Subsystem
Mission Objective & Evaluated Solutions
The goal of this subsystem is to autonomously detect, accurately pick up a plastic bottle from uneven outdoor terrain, and successfully drop it into the designated onboard storage bin.
Solution 1
Robotic Arm
Solution 2
Conveyor Belt
A motorized sliding base that moves a collector along a track. Pros: Simple to build. Cons: Restricted to 2D movement and consumes massive battery power fighting friction.
Solution 3
Vacuum Pickup
A robotic arm that uses a suction pad to grab items. Pros: Easy grabbing. Cons: Highly unstable; causing it to drop bottles.
An articulated arm with gripper. Pros: Full 3D spatial reach, smooth movement, and tight grip. Selected as our main proposed solution.
13

## Slide 14
Comparison & Final Selection — Waste Pickup
Criteria | Robotic Arm | Conveyor Belt | Vacuum
Path Accuracy (RMSE) | 0.0020 rad | 0.0150 m | 0.0350 rad
Avg. Settling Time | 0.85 s | 2.15 s | 3.80s
Peak Actuator Torque | 0.55 Nm (Safe) | 12.5 N(Friction) | 0.85 Nm (Heavy)
Total Motor Energy | 28.4 Joules | 55.6 Joules | 142.5 Joules
Workspace Reach | 3D Spatial (Flexible) | 2D Plane | 3D Spatial
Hardware Cost (Est) | ৳ 7,430 BDT | ৳ 3,500 BDT | ৳ 8,000 BDT
✅ Selected Solution: Gripping Arm Mechanism
14

## Slide 15
Gripping Arm
Hardware Specifications
Structure: 18 × 18 × 6 cm
Actuator: Servo Motor MG996R
Motor Driver: PCA9685
Gear Type: Metal Gear
MCU: Arduino Uno
15

## Slide 16
Refined Design
📡
Navigation
Lidar Sensor and camera (360° Rotation environment Scanning and Detect Obstacles )
🎯
Detection
YOLOv8n Deep Learning Model(Detects obstacles and plastic waste simultaneously)
⚙️
Pickup
Gripper method (Servo-controlled arm, precise pickup, adaptable to different positions)
System Features
Autonomous navigation with 360° sensing
Real-time plastic detection
Precise robotic arm pickup
Secure storage & safe disposal
16

## Slide 17
Refined System Design Specifications
Complete system - 7 integrated subsystems
⚡
Power Management Unit — 24V Li-ion, DC-DC buck converters, fuse protection
👁️
Detection & Perception Unit — YOLOv8n model, 720p camera, RPLiDAR A1
🧠
Control & Processing Unit — Raspberry Pi 4 (4GB) + Arduino UNO & Nano via UART
🚗
Navigation & Mobility Unit — Differential drive, L298N, IMU MPU6050, encoders
🦾
Waste Collection Mechanism — Robotic arm, MG996R servos, mechanical gripper, Arduino UNO
🗃️
Storage & Disposal Unit — Onboard bin, optional fullness sensor (HX711)
🛡️
Safety & Auxiliary Unit — Emergency stop, LED indicators, buzzer.
17

## Slide 18
Overall System Performance
Final system evaluation across key criteria
Criteria | Performance
Accuracy | High
Cost Efficiency | High
Complexity | Medium
Speed | Medium
Reliability | High
Real-time Response | High
18

## Slide 19
Refined System Circuit Diagram
19

## Slide 20
Refined System Circuit Diagram
20

## Slide 21
Thank You
Autonomous Plastic Waste Collector Robot
EEE400B — East West University
Questions & Discussion
21

## Slide 22
Appendix

## Slide 23
Appendix

## Slide 24
Appendix

## Slide 25
Appendix

## Slide 26
Appendix

## Slide 27
Appendix

## Slide 28
Appendix: Specification
Subsystem | Component | Specification | Function
Power Management | Li-ion Battery Pack | 24 V, 6–8 Ah | Main power source
Power Management | BMS | 24 V / 7S Li-ion BMS | Battery protection
Power Management | Battery Charger | 29.4 V, 2 A CC/CV Li-ion charger | Charges 24 V battery pack
Power Management | Main Switch | 24 V DC rated | System ON/OFF control
Power Management | Fuse Protection | 10–15 A DC fuse | Overcurrent protection

## Slide 29
Appendix: Specification
Subsystem | Component | Specification | Function
Power Management | Buck Converter | 24 V to 5 V, 5 A | Supplies Pi, Arduino, sensors, display
Power Management | Buck Converter | 24 V to 12 V, 5–10 A | Supplies DC motors
Power Management | Buck Converter | 24 V to 6 V, 5–10 A | Supplies servo motors
Control | Raspberry Pi 4 | 4 GB RAM | Runs YOLOv8n, navigation logic, decision-making
Control | Arduino Nano | ATmega328P, 5 V logic | Handles sensors, encoder input, mobility control
Control | Arduino UNO | ATmega328P, 5 V logic | Dedicated arm and gripper controller

## Slide 30
Appendix: Specification
Subsystem | Component | Specification | Function
Control | microSD Card | 32–64 GB, Class 10 | Stores OS, code, model, logs
Control | Cooling Fan + Heatsink | Pi cooling system | Prevents overheating
Communication | UART Serial | Pi-to-Arduino communication | Exchanges commands and status
Communication | Logic Level Shifter | 3.3 V / 5 V compatible | Protects Raspberry Pi GPIO
Detection | Camera Module | 720p USB/Pi camera | Captures images for plastic detection

## Slide 31
Appendix: Specification
Subsystem | Component | Specification | Function
Perception | RPLiDAR A1 | 360° LiDAR | Environmental scanning
Perception | Ultrasonic Sensors | US-100 / HC-SR04 | Short-range obstacle detection
Mobility | DC Gear Motors | 12 V geared DC motors | Drives robot wheels
Mobility | Motor Driver | L298N or equivalent | Controls motor speed and direction
Mobility | Wheels | 80–100 mm rubber wheels | Provides traction
Mobility | Caster Wheel | Support wheel | Maintains balance
Mobility | Wheel Encoders | LM393 modules | Measures wheel rotation

## Slide 32
Appendix: Specification
Subsystem | Component | Specification | Function
Mobility | IMU | MPU6050 | Measures orientation and motion
Collection | Robotic Arm | Prototype arm / multi-DOF design | Positions gripper
Collection | Servo Motors | MG996R metal gear servos | Moves arm joints and gripper
Collection | Mechanical Gripper | Servo-operated end effector | Grasps plastic waste
Collection | Arm Mounting Bracket | Acrylic/metal mount | Fixes arm to chassis
Storage | Storage Bin | Plastic/acrylic bin | Stores collected waste
Storage | Fullness Sensor | HX711 load cell or ultrasonic level sensor | Detects bin-full condition

## Slide 33
Appendix: Specification
Subsystem | Component | Specification | Function
Disposal | Dumping Mechanism | Manual or servo-assisted unloading | Transfers waste to central bin
Safety | Emergency Stop | NC push button | Immediately stops the robot
Safety | LED Indicators | Red/green/yellow LEDs | Shows system status
Safety | Buzzer | 5 V active buzzer | Provides warning sound
Auxiliary | OLED Display | 0.96-inch SSD1306 I2C, 128×64, 3.3–5 V | Displays mode, battery, detection, and error status
Structure | Chassis | 550 mm × 400 mm base, acrylic/metal | Main robot frame

## Slide 34
Appendix: Specification
Subsystem | Component | Specification | Function
Structure | Protective Cover | Acrylic/plastic/metal enclosure | Protects electronics
Structure | Bumper Guard | Front impact guard | Reduces collision damage
Structure | Mounting Hardware | Nuts, bolts, brackets, spacers | Mounts all components
Wiring | Jumper Wires / Connectors | Signal and power wiring | Connects electronics
Wiring | Breadboard / PCB | Prototype or soldered PCB | Supports circuit integration